EDR　Series

Model

ECOMaster

Service Manual

Rev 1.0　(Preliminary)

Contents

1. Maintenance Operations	5

1.1 Maintenance Mode	6

1.2 Basic knowledge of Parameters	8

1.2.1 Mechanical Resolutions	8

1.2.2 Preparation of checking mechanical movement based on Parameters	8

1.2.3 The meaning of the explanation symbols.	8

1.3 Program Parameters	9

1.3.1 Polish	10

1.3.1-1 Process with pads	11

1.3.1-2 Sanding Time 1	11

1.3.1-3 Sanding Time 2	11

1.3.1-4 Sanding Motor rpm	12

1.3.1-5 Sanding Pressure	12

1.3.1-6 Platen Motor rpm	12

1.3.1-7 Platen Start Height	12

1.3.1-8 Contact Adjustment	12

1.3.1-9 Water P or Compound P Working Time	12

1.3.1-10 Washing Time	12

1.3.1-11 Drying Time	13

1.3.1-12 CoatingP Working Time	13

1.3.2 Platen Lift	14

1.3.2-1 Platen Lift - Disc Release Height	14

1.3.2-2 Platen Lift - Turret Turn Height	15

1.3.2-3 Platen Lift - Disc Grab Height	15

1.3.3 Grabs	16

1.3.3-1 Grabs - Release Cartridge	16

1.3.3-2 Grabs - Moving Cartridge	17

1.3.3-3 Grabs - Disc Sensor	17

1.3.3-4 Grabs - Release Platen	18

1.3.3-5 Grabs - Origin Sensor	18

1.3.3-6 Grabs – Home	18

1.3.4 Cartridge	19

1.3.4-1 Cartridge - Pick Up Lower	19

1.3.4-2 Cartridge - Disc In	20

1.3.4-3 Cartridge - Disc Out Before	21

1.3.4-4 Cartridge - Disc Out After	22

1.3.4-5 Cartridge – Origin	22

1.3.5 Timers	23

1.3.6 Mode	24

1.3.7 Water Recycle	25

1.4 Manual operation	26

1.5 Statistics	31

1.6 Adjust Touch Panel	34

1.7 Date and Time	36

2. Hardware	37

2.1 Block diagram	38

2.2 Function explanation of each electrical board	39

2.2.1 Main Board (EM-P01)	39

2.2.2 LCD Board (EM-P02)	46

2.3 Maintenance Tool	47

2.4 Contact pins	48

2.5 Power Supply Connector	49

3. Mechanical Module	50

3.1 Abrasive Unit	51

3.2 Loading Unit	52

3.3 Platen Unit	53

3.4 Changer Unit	54

3.5 Pump and Water Recycle Unit	55

4. Trouble shooting	56

4.1 Trouble of the finishing	57

4.1.1 When water remains on the center of disc	57

4.1.2 When compound remains on the center of disc	57

4.1.3 The surface of disc that it was completed is generally white	58

4.1.4 The scar that a bubble bursts open is left on the disc	58

4.1.5 When the scratches can be recognized clearly remain like straight line on the disc	58

4.1.6 When fine scratches can't be recognized clearly remain on the whole of the disc	59

4.2 Trouble of the others	60

4.2.1 When Platen Motor vibrates while rotates	60

4.2.2 When the Disc was not picked up	61

4.2.3 When two Discs was picked up together	61

4.2.4 When water becomes muddy in the Water Recycle System	62

4.2.5 When the Water or Compound don’t come out	62

# 1. Maintenance Operations

## 1.1 Maintenance Mode

When you want to enter the maintenance mode, keep pushing the [POWER/PAUSE] Switch after turning ON the power until below screen is displayed. Enter password and touch “E” then.

The machine starts to initialize if you touch “Cancel” in this screen.

Operations in Touch Panel for maintenance are authorized service technicians only.

The menu for maintenance is displayed if you enter correct password.

In this screen, you can recognize Software version and IP address of this machine.

The machine starts to initialize when you touch “Return” in this screen.

Program Parameters	See… 1.3 Program Parameters

Manual Operation		See… 1.4 Manual Operation

Statistics		See… 1.5 Statistics

Adjust Touch Panel	See… 1.6 Adjust Touch Panel

Date and Time		See… 1.7 Date and Time

## 1.2 Basic knowledge of Parameters

When a parameter is changed, it is necessary to understand that meaning fully.

### 1.2.1 Mechanical Resolutions

Platen Lift ----0.006 mm/pulse

Grabs ---------0.020 mm/pulse

Cartridge -----0.095 mm/pulse

### 1.2.2 Preparation of checking mechanical movement based on Parameters

- Remove the Back Cover.

- Confirm whether two knobs that fix Changer Unit are being installed.

- Push the [STEP] button, which exists in a Manual Operation page 3/5, and proceed to Parameters Mode.

### 1.2.3 The meaning of the explanation symbols.

[LN] : push the Loading NEXT button.

[LB] : push the Loading BACK button.

[PN] : push the Platen Lift NEXT button.

[PB] : push the Platen Lift BACK button.

[CN] : push the Cartridge NEXT button.

[CB] : push the Cartridge BACK button.

Example		[LN][LN] : push the Loading NEXT button twice.

## 1.3 Program Parameters

The Menu of items to set up is displayed. If you touch “SAVE” after entering each parameter then it will be preserved. You don’t have to change parameters because they were set up in advance. Be careful not to enter different parameter because the machine may not work normally.

“Polish” 		: Parameters of polish

Below 3 items are different in every machine.

“Platen Lift” 	: Parameters of Mechanical movement for Platen Lift

“Grabs”		: Parameters of Mechanical movement for Grabs

“Cartridge” 	: Parameters of Mechanical movement for Cartridge

“Timers” 	: The exchange time of the part with the life

“Mode” 		: Machine Mode

“Water Recycle” 	: Parameters of Water Recycle

“Send”		: No use

“Recv”		: No use

“SAVE”		: Changed parameters are kept.

### 1.3.1 Polish

The menu of each Pad to set up parameters is displayed. The screen to do will be displayed if you touch each “Pad”.

The list of parameters connected with polish of Pads.

The screen to enter the value will be displayed if you touch the number part.

The same setup item exists about all PAD's.

#### 1.3.1-1 Process with pads

There are maximum 6 processes in repairing. The pad used in each process is as the next.

| Process Number | 5 | 4 | 3 | 2 | 1-2 | 1-1 |
| --- | --- | --- | --- | --- | --- | --- |
| Pad | BLUE | RED | GREEN | YELLOW | BLACK | BLACK |
| Solution | Water | Water | Water | Water | Water | Compound |

#### 1.3.1-2 Sanding Time 1

- This is the time of sanding motor CW rotation in all process.

- When the Sanding Pressure reached to desired value, sanding time will count.

- The water pump is working in process number from 5 to 1-2 at the same time.

- In process number 1-1, The compound pump is working based on the parameter of ‘Water P or Compound P Working Time’

#### 1.3.1-3 Sanding Time 2

- This is the time of sanding motor CCW rotation in process number from 5 to 2.

- When the Sanding Pressure reached to desired value, sanding time will count.

- Default parameter is 0 sec at the process number 5, 4 and 1-1.

- The water pump is working in process number from 5 to 2 at the same time.

- In process number 1-2, time is used for drying of wet sponge then sanding motor rotates CW rotation.

#### 1.3.1-4 Sanding Motor rpm

- Set the revolution number of sanding motor.

- The pad can rotate 2000 rpm when the value is 100%.

#### 1.3.1-5 Sanding Pressure

- Set the sanding pressure.

- When the value is 100%, Platen Lift will continue the rise until motors ampere reaches to 5A.

- You must set it on less than 42% because rated current ampere of sanding motor is 2.1A.

#### 1.3.1-6 Platen Motor rpm

- Set the revolution number of platen motor.

- The turn table can rotate 1500 rpm when the value is 100%.

- You must set it on less than 55% because platen motor occurs ‘Motor Locked’ error.

#### 1.3.1-7 Platen Start Height

- Set it up in accordance with the next rule.

<Formula>   Platen Start Height = ‘Contact Adjustment’ – Constant value

| Process Number | 5 | 4 | 3 | 2 | 1-2 | 1-1 |
| --- | --- | --- | --- | --- | --- | --- |
| Constant value | 300 | 300 | 500 | 500 | 500 | 800 |

#### 1.3.1-8 Contact Adjustment

- The first value is set automatically when you select Platen Lift Teaching.

- The next value is range of contact height of a pad and a disc.

For example, the first value is 10200 and next one is 2000. In this case, the pad and the disc must contact from 8200 to 12200 height, otherwise ‘ No Sanding Pad’ or ‘Any Disc Release’ error occurs.

#### 1.3.1-9 Water P or Compound P Working Time

- This parameter is only use at process number 1.

- It is the compound working time. The amount of Compound gives it a great influence to the disc finish.

#### 1.3.1-10 Washing Time

- Time setting for washing process after abrasion process.

Default values are zero.

#### 1.3.1-11 Drying Time

- Time setting for drying process after abrasion process.

Default values are zero.

#### 1.3.1-12 CoatingP Working Time

- Time setting for Coating Pump working time.

If there is no Coating Option in a machine, you don’t need set any parameters of Coating.

### 1.3.2 Platen Lift

The list of the parameter about the movement of the Platen Lift is indicated.

When the numerical value of an item to change is stamped, a data input screen is indicated, and a set point can be changed.

#### 1.3.2-1 Platen Lift - Disc Release Height

| Default value | 1400 pulse |
| --- | --- |
| Explanation | Grabs release a disc when platen table is this height. |
| Operations | [LN][LN] (Release Platen) Open the Hatch and a disc is put between the grabs. Close the hatch. [PN](Disc Release Height) It is observed from the rear of the main body. Confirm whether the center pin projects in comparison with disc. (About 3 to 5mm) |

#### 1.3.2-2 Platen Lift - Turret Turn Height

| Default value | 6100 pulse |
| --- | --- |
| Explanation | During turret motor moving, platen table goes down to this height to avoid pads and sponge. |
| Operations | [PN] [PN] [PN] (Turret Turn Height) Push the [RETURN] button, then push the [↑] twice. (Manual Operation page 1/5) Push the Turret Motor [ON] button. It is observed from the rear of the main body. Confirm that black sponge does not touch splash cover. |

#### 1.3.2-3 Platen Lift - Disc Grab Height

| Default value | 2140 pulse |
| --- | --- |
| Explanation | Grabs catch a disc from platen table. If this height is too high or low, grabs cannot catch the disc rightly and ‘Disc Unloading Error’ occurs. |
| Operations | Open the hatch. Put a disc on the turn table. Then close the hatch. [PN][PN](Disc Grab Height) [LN] [LN] (Release Platen) Loosen Changer’s two knobs, and open the Changer Unit. It is observed from the rectangle window. Confirm whether the groove of Roller agrees to Disc. |

### 1.3.3 Grabs

The list of the parameter about the movement of the Grabs is indicated.

When the numerical value of an item to change is stamped, a data input screen is indicated, and a set point can be changed.

#### 1.3.3-1 Grabs - Release Cartridge

| Default value | 8530 pulse |
| --- | --- |
| Explanation | When the grabs receive a disc from pickup, and when grabs return a disc to spindle, loading unit stops at this value. |
| Operations | [LN] [LN] [LN] [LN] [LN] (Release Cartridge) Open the Changer door. A disc is put between the grabs. Confirm whether the disc hole agrees to shaft. |

#### 1.3.3-2 Grabs - Moving Cartridge

| Default value | 2915 pulse |
| --- | --- |
| Explanation | When pickup is moving, the grabs are waiting at this value. |
| Operations | [LN] [LN] [LN] (Moving Cartridge) Open the Changer door. Confirm that Grabs being inside the main body. |

#### 1.3.3-3 Grabs - Disc Sensor

| Default value | 3900 pulse |
| --- | --- |
| Explanation | The position of the grabs to confirm whether disc is held. |
| Operations | [LN] [LN] [LN] [LN] [LN] (Release Cartridge) Open the Changer door. A disc is put between the grabs. [LB] (Disc Sensor) Confirm whether the sensor monitor turn on. Monitor color is RED. GREEN monitor symbolize the stability of the light. |

#### 1.3.3-4 Grabs - Release Platen

| Default value | 610 pulse |
| --- | --- |
| Explanation | The position where the grabs is releasing a disc and catch a repaired one. |
| Operations | [LN] [LN] (Release Platen) Open the hatch. A disc is put between the grabs. Confirm whether the disc hole agrees to the Center Pin. |

#### 1.3.3-5 Grabs - Origin Sensor

| Default value | 100 pulse |
| --- | --- |
| Explanation | Origin sensor is checked at this position. |
| Operations | [LN] (Origin Sensor) Confirm that the origin sensor monitor is turn on. Usually this parameter is not change. |

#### 1.3.3-6 Grabs – Home

| Default value | 0 pulse |
| --- | --- |
| Explanation | Most returned position of the loading unit. |
| Operations | Never change this parameter. |

### 1.3.4 Cartridge

The list of the parameter about the movement of the Cartridge is indicated.

When the numerical value of an item to change is stamped, a data input screen is indicated, and a set point can be changed.

#### 1.3.4-1 Cartridge - Pick Up Lower

| Default value | 2135 pulse |
| --- | --- |
| Explanation | Full stroke of the Pick Up. |
| Operations | Confirm that there is no disc in stocker of the Changer Unit. [CN] [CN] [CN] [CN] (Pick Up Lower) Confirm that sensor monitor is turn on and whether Stocker table can descend approx 1 mm. (Push it by finger and check it.) |

#### 1.3.4-2 Cartridge - Disc In

| Default value | 105 pulse |
| --- | --- |
| Explanation | Height that grabs receive a disc. |
| Operations | Push the [RETURN] button, and then push the Vacuum [ON] button. A disc absorbs to the Vacuum Pad. Push the [STEP] button. [CN] (Disc In) [LN] [LN] [LN] [LN] [LN] (Release Cartridge) Confirm whether the height of disc agrees to the groove of Roller. |

#### 1.3.4-3 Cartridge - Disc Out Before

| Default value | 1250 pulse |
| --- | --- |
| Explanation | The Spindle is waiting this position during the grabs carries a repaired disc. |
| Operations | [CN] [CN] [CN] (Disc Out Before) [LN] [LN] [LN] [LN] [LN] (Release Cartridge) A disc is put between the grabs. Confirm that distance between spindle to disc is approx 10mm. |

#### 1.3.4-4 Cartridge - Disc Out After

| Default value | 1150 pulse |
| --- | --- |
| Explanation | Spindle goes to this position after the grabs carried a disc. |
| Operations | [CN] [CN] [CN] (Disc Out Before) [LN] [LN] [LN] [LN] [LN] (Release Cartridge) A disc is put between the grabs. [CB] (Disc Out After) Confirm whether the Spindle projects in comparison with disc. (Approx 3mm) |

#### 1.3.4-5 Cartridge – Origin

| Default value | 0 pulse |
| --- | --- |
| Explanation | Upper limit of the Pick Up. |
| Operations | Never change this parameter. |

### 1.3.5 Timers

The list of the Timers is indicated.

When the numerical value of an item to change is stamped, a data input screen is indicated, and a set point can be changed.

### 1.3.6 Mode

The list showing motion modes of the machine is displayed. Touch “ON” or “OFF” of each item if you want to change settings of the machine. Set all items “OFF” at usual automatic operations. It is used to check motions of the machine or do initial settings.

| Display Equipment Condition | The value of electric current to polish, and so on are displayed. |
| --- | --- |
| Platen Lift Teaching | In this mode, the machine input itself average contact height of each pad and a disc into Contact Adjustment. You have to return to menu screen, otherwise, the machine can’t input that number. |
| Cartridge Test: | Motions of Cartridge is checked. In this mode, the machine input distance from Cartridge origin to the1st disc itself. Also the machine can’t input that number without returning to menu screen. |
| Coating Option | Set this item “ON” in using the machine with Coating Option. |
| Water Recycle System | Set this item “ON” in using the machine with Water Recycle System. |

*If the Platen Lift Teaching and Cartridge Test are ON at same time, the machine does Cartridge Test.

### 1.3.7 Water Recycle

The list of parameters connected with Water Recycle System. The screen to enter the value will be displayed if you touch the number part.

| Power ON/OFF Interval | The time of 1 period to drive water recycles system. |
| --- | --- |
| Off Time | The rate of off time in the “Power ON/OFF Interval” period. |
| Follow Time(Start) | Time to work for a water pump after to stop. (Start) |
| Follow Time(Minimum) | Time to work for a water pump after to stop. (Minimum) |
| Decrease Follow Time | No use |
| Decrease Interval | No use |
| Ampere | No use |

## 1.4 Manual operation

You can operate each motor and so on, and check motions of them.

Operate each motor after confirming if each part doesn’t hit one another.

*Be careful there is no safety lock in this mode.

Turret Motor 	: ON/OFF Switch for Turret Motor.

Water Recycle	: ON/OFF Switch for Water Recycle.

You can confirm whether Water Recycle works normally by using this switch.

Normally almost 6.0V and over 1.0A indicated with keeping “ON”.

If you get over 11.0V and 0.0A indicated even though keeping “ON”, there are possibilities Reactive pipe isn't connected or no water in 1st tank.

If you get 0.0V and 0.0A indicated even though keeping “ON”, there are possibilities Reactive pipe is touching the Outer pipe.

Water Pump	: ON/OFF Switch for Water Pump with Fast/Slow mode.

Compound	: ON/OFF Switch for Compound Pump.

Coating		: ON/OFF Switch for Coating Pump.

“C W”: Sanding Motor rotates clockwise.

“CCW”: Sanding Motor rotates counterclockwise.

Sanding Motor	: ON/OFF Switch for Sanding Motor with CW/CCW direction.

Platen Motor	: ON/OFF Switch for Platen Motor.

Touching the number of % value can change speed of the motor.

RESET         : When the error occurs from PIC it is controller for both motor, error can be reset by this switch.

| Ov | Cu | * | * | Rd |
| --- | --- | --- | --- | --- |
| Over Load Error | Wire disconnection | No use | No use | Ready |

AD=            : Motor current value 1023=5[A](Max)

Cartridge, Loading, Platen Lift: Stepping motor movement.

Vacuum		: ON/OFF Switch for Vacuum pump.

Endurance test	: It uses for the machine endurance test.

STEP		: It uses to confirm a machine movement in the parameter.

Refer to below screen for Endurance test.

Each unit moves continuously with “CON” button.

The movement number of times is counted and indicated.

This counter is reset by “Clear” button.

Refer to below screen for STEP movement.

Each unit moves to the position of setting parameter with  “BACK” and “NEXT” button.

Name of parameter and value are indicated in the screen.

“  ”: The sensor is now at work.

“  “: The sensor isn’t now at work.

This screen is for testing the Hardware, in maintenance not use.

## 1.5 Statistics

The menu of items to confirm is displayed. You can check total user count of each disc, total work time of each motor and so on.

“CD”: Total user count of CD is displayed each mode.

“DVD”: Total user Count of DVD is displayed each mode.

“**”: No Use.

“Motors”: Total work time of each motor is displayed.

“Errors”: Each error count is displayed.

## 1.6 Adjust Touch Panel

The screen to check coordinates of Touch Panel is displayed. If you touch “  ” mark in the center of the screen, coordinates of that point will be displayed. If coordinates displayed are too different from actual values, touch “Calibration” and correct them.

Calibration

The screen to enter the values of coordinates is displayed. Touch the tip of each arrow once in the numerical order. Coordinates will be set up and previous screen will be displayed after touching the arrow 4. Touch “×” mark to confirm if they are set up rightly.

In the case of failure of calibration

At first turn off the power and set the DIP Switch on Main board for “Touch Panel Calibration mode”

<Procedure>

    - Turn off the power.

    - DIP SW2 bit 7 is ON.

    - Turn on the power.

    - Try again calibration.

    - After getting success, turn off the power.

    - DIP SW2 bit 7 is OFF.

## 1.7 Date and Time

Date and Time can be changed.

# 2. Hardware

In this section, the structure of the electricity and an attention point in maintenance are mentioned.

Take care of static electricity when you deal with an electronic circuit board.

Before removing the electronic circuit board and the connector for maintenance, turn off the Main power.

## 2.1 Block diagram

## 2.2 Function explanation of each electrical board

### 2.2.1 Main Board (EM-P01)

| 1 | CPU |
| --- | --- |
| 2 | EEPROM |
| 3 | SRAM |
| 4 | PIC |
| 5 | Sensor Interface |
| 6 | LCD Interface |
| 7 | DC Motor Drivers |
| 8 | Stepping Motor Drivers |
| 9 | 7Seg LED |
| 10 | DIP Switch |
| 11 | Reset Switch |
| 12 | FROM (Backside) |

DIP SW1 (For Operating system)

1: Program mode

2: Reserved

3: EEPROM clear (OS area)

4: WDT test mode

5: No Use

6: No Use

7: No Use

8: No Use

DIP SW2 (For Application)

1: Ignore EEPROM error

2: All Counters clear (With Maintenance mode)

3: No Use

4: No Use

5: No Use

6: No Use

7: Touch Panel Calibration mode

8: Initialize all parameters (With Maintenance mode)

<Connectors>

| 1 | CN1 | Xilinx JTAG connector (For test) |
| --- | --- | --- |
| 2 | TCN1 | SH test connector (For test) |
| 3 | CN2 | Ethernet connector |
| 4 | CN3 | SH JTAG connector (For test) |
| 5 | CN5 | Sensor connector |
| 6 | CN10 | DC Power connector |
| 7 | CN14 | Stepping motor connector |
| 8 | CN13 | Power in connector |
| 9 | CN12 | Sanding parts connector |
| 10 | CN11 | Pump connector |
| 11 | CN9 | Vacuum motor connector |
| 12 | CN6 | LCD connector |
| 13 | CN4 | RS-232C connector |

### 2.2.2 LCD Board (EM-P02)

| 1 | LCD Controller |
| --- | --- |
| 2 | Buzzer |
| 3 | Touch Panel Controller |
| 4 | LCD Back Light Inverter |
| 5 | LCD Interface |
| 6 | 5VPS |
| 7 | 12VPS2 (Water recycle) |
| 8 | 12VPS1 (Water pump) |
| 9 | 3.3VPS |

## 2.3 Maintenance Tool

| 1 | 57031-6000 (Molex) |
| --- | --- |
| 2 | J5800-005 (Molex) |
| 3 | JHTR2262A (Molex) |

## 2.4 Contact pins

## 2.5 Power Supply Connector

CNPS: 5557-08R (Molex)

| Pin No. | Assign |
| --- | --- |
| 1 | 26VGND |
| 2 | 26VGND |
| 3 | 5VsbGND |
| 4 | 5Vsb |
| 5 | 26V |
| 6 | 26V |
| 7 | PS-ON |
| 8 | PWR-OK |

# 3. Mechanical Module

## 3.1 Abrasive Unit

## 3.2 Loading Unit

## 3.3 Platen Unit

## 3.4 Changer Unit

## 3.5 Pump and Water Recycle Unit

# 4. Trouble shooting

## 4.1 Trouble of the finishing

### 4.1.1 When water remains on the center of disc

| Cause | Center seal doesn't relate to disc closely completely. |
| --- | --- |
| Action | Attach Center seal to sleeve of the metal securely. Attach Center seal securely to sleeve of the metal. Confirm whether pressure spring works normally. For example, Doesn't Retaining ring come off? Does a Slide mechanism work smoothly? |

### 4.1.2 When compound remains on the center of disc

| Cause | There may be much amount of compound. |
| --- | --- |
| Action | Remove Back-cover, and observe a state during grinding. Confirm whether compound doesn't come out at the timing when originally it must not work. |

| Cause | A foreign substance may stick to the tip of the nozzle. |
| --- | --- |
| Action | Clean up the tip of the nozzle. |

### 4.1.3 The surface of disc that it was completed is generally white

| Cause | In case of white dirt is removed if it is wiped with a finger, it is shortage of wipe of the compound. |
| --- | --- |
| Action | Increase the number of settings it is “Sanding Timer1” or “Sanding Pressure”. |

| Cause | In case of white dirt is not removed if it is wiped with a finger, it is wiped out too much. |
| --- | --- |
| Action | Decrease the number of settings it is “Sanding Timer1” or “Sanding Pressure”. |

### 4.1.4 The scar that a bubble bursts open is left on the disc

| Cause | Black sponge touches the splash cover when lift goes down. |
| --- | --- |
| Action | Confirm whether there is burr around the hole of splash cover. |

### 4.1.5 When the scratches can be recognized clearly remain like straight line on the disc

| Cause | Particle sticks to Black Pad. There are many cases that the fragment of Velcro fastening specially sticks. |
| --- | --- |
| Action | Wash Black Pad in water, and get rid of particle, or exchange it for the fresh one. |

### 4.1.6 When fine scratches can't be recognized clearly remain on the whole of the disc

| Cause | It is likely to damage it with edge of pad (especially, Yellow pad). |
| --- | --- |
| Action | Observe edge of each pad well. Then, exchange it for new pad if pad with the problem is discovered. |

## 4.2 Trouble of the others

### 4.2.1 When Platen Motor vibrates while rotates

| Cause | A rotation shaft was likely to lean in some causes. Turn a motor with Manual Operation, and confirm deflection of the shaft. |
| --- | --- |
| Action | Open hatch, and correct deflection carefully. |

### 4.2.2 When the Disc was not picked up

| Cause | Water and compound may stick to disc. |
| --- | --- |
| Action | Wipe both sides of disc with waste cloth. |

| Cause | It may be choked with transparency tube and vacuum pump and filter. Start Pump with Manual Mode, and block vacuum hole with the finger. Do you feel pressure with the fingertip? |
| --- | --- |
| Action | Confirm whether tube isn't bent halfway. Next, clean filter. Exchange pump if still it doesn't recover. |

### 4.2.3 When two Discs was picked up together

| Cause | It has possibility with thin disc of the thickness in the cartridge. |
| --- | --- |
| Action | Don't set disc of the thickness 1mm and under. |

| Cause | Water and compound may stick to disc. |
| --- | --- |
| Action | Wipe both sides of disc with waste cloth. |

### 4.2.4 When water becomes muddy in the Water Recycle System

| Cause | Outer Pipe and Inner Pipe don't touch each terminal properly, and it isn't likely to be charged with proper electricity. |
| --- | --- |
| Action | Set the Water Recycle System properly. |

### 4.2.5 When the Water or Compound don’t come out

| Cause | It has the possibility that tube is bent. |
| --- | --- |
| Action | Remove Water Recycle System unit, and confirm whether there is a wrong point in piping. |

| Cause | It has the possibility that tube inside pump is transformed when it doesn't work in the machine and it is left in the long period. When it drives in the cold districts, a liquid freezes, and a pump output shaft made of the plastic is likely to be damaged. |
| --- | --- |
| Action | Remove the blue cap of pump, and observe the inside. Exchange it for pump if there is a problem in Pump. |

# Text boxes

WARNING! :

Carefully read and thoroughly understand the important warning items described in this manual before maintaining this unit.

Password

Please

Enter

Password

Warning:

Authorized

Service Technician

Only

Cancel

0

7

8

9

4

5

6

1

2

3

0

C

E

Maintenance

IP

192.168. 1. 1            2003/4/18  Version 1.10

Return

Statistics

Manual Operation

Program Parameters

Date and Time

Adjust Touch Panel

Maintenance

Program Parameters

SAVE

Polish

Grabs

Timers

Water Recycle

Platen Lift

Cartridge

Mode

Send

Recv

Maintenance

Program Parameters

Polish

Pad #5

Pad #3

Pad #1-2

Coating

Pad #4

Pad #2

Pad #1-1

Return

Maintenance

Program Parameters

Polish

Sanding Time1

Sanding Time2

Sanding Motor rpm

Sanding Pressure

Platen Motor rpm

Platen Start Height

Contact Adjustment

WaterP Working Time

(CompoundP Working Time)

(CoatingP Working Time)

Washing Time

Drying Time

Return

0

25

10200

10757±

0

0

30

45

20

0

0

Sec

Sec

%

%

%

Pulse

Pulse

Sec

Sec

Sec

Maintenance

Program Parameters

Platen Lift

Disc Release Height

Turret Turn Height

Disc Grab Height

Return

6100

1400

2300

Pulse

Pulse

Pulse

## 3 to 5mm

Disc

Roller

Maintenance

Program Parameters

Grabs

Release Cartridge

Moving Cartridge

Disc Sensor

Release Platen

Origin Sensor

Home

Return

2915

610

0

8530

3900

100

Pulse

Pulse

Pulse

Pulse

Pulse

Pulse

Shaft

Sensor

Maintenance

Program Parameters

Cartridge

Pick Up Lower

Disc In

Disc Out Before

Disc Out After

Origin

Return

105

1150

2135

1250

0

Pulse

Pulse

Pulse

Pulse

Pulse

Sensor

## 10mm

## 3mm

Maintenance

Program Parameters

Timers 1/3

Water

1st Filter(1)

1st Filter(2)

Al Pipe

Compound

Coating

Return

450

5000

70

Hour

Min

Min

Min

Sec

Sec

47

24

250

Timers 2/3

Pad #5

:

Pad #0

20

100

Min

Min

Maintenance

Program Parameters

Timers 3/3

Sanding Motor

Platen Motor

Water Pump Motor

Compound Pump Motor

Coating Pump Motor

Vacuum Pump Motor

3000

1500

250

2000

1500

1500

Hour

Hour

Hour

Hour

Hour

Hour

Maintenance

Program Parameters

Mode

Display Equipment Condition

Platen Lift Teaching

Cartridge Test

Coating Option

Water Recycle System

Return

ON

OFF

ON

OFF

ON

OFF

ON

OFF

ON

OFF

Maintenance

Program Parameters

Water Recycle

Power ON/OFF Interval

Off Time

Follow Time(Start)

Follow Time(Minimum)

Decrease Follow Time

Decrease Interval

Ampere

Return

30

10

0

2

10

0

0.0

Sec

%

Sec

Sec

Sec

Min

A

Maintenance

Manual Operation 1/5

0.0A    0.0V

Turret Motor           Water Recycle

Water Pump          Compound     Coating

Return

ON

OFF

ON

OFF

ON

OFF

ON

OFF

ON

Fast

Slow

Maintenance

Manual Operation 2/5

100%

Sanding Motor　　　　 Platen Motor

ON

OFF

ON

OFF

C W

CCW

RESET

** ** ** ** Rd

OvCu ** ** Rd

AD =  6

AD =  6

OvCu ** ** Rd

Maintenance

Manual Operation 3/5

Cartridge                            Platen Lift

UP

STOP

DOWN

UP

STOP

DOWN

IN

STOP

OUT

Loading

0                 0                 0

STEP

Endurance test

ON

OFF

Vacuum

Maintenance

Endurance test

Cartridge                           Platen Lift

CON

OFF

Clear

Loading

Return

CON

OFF

Clear

CON

OFF

Clear

Go and Back

0 Count

Go and Back

0 Count

Go and Back

0 Count

Maintenance

Parameters Move

Cartridge                           Platen Lift

BACK

STOP

Loading

0                 0                 0

Return

NEXT

NEXT

BACK

STOP

BACK

STOP

NEXT

Origin 	    Home 	      Unlock

Maintenance

Manual Operation 4/5

Sensor Condition

Splash Cover

Disc Motor

Turret Arrival

Turret Origin

Grabs Origin

Machine Door

Cartridge Door

Hatch Close

Lift Origin

* * * * * * * *

* * * * * * * *

Cartridge Origin

Cartridge Lower

Disc Out

* * * * * * * *

Fan Alarm

Maintenance

Manual Operation 5/5

Main Board Condition

ON

OFF

Fan

ON

DIP SW1

1

0

8

7

6

5

4

3

2

1

Water Leak

Pump Flow1

Pump Flow2

Pump Flow3

ON

DIP SW2

1

0

8

7

6

5

4

3

2

1

Maintenance

Statistics

Return

DVD

CD

* *

Motors

Errors

Return

600Count

1500Count

2000Count

1200Count

1200Count

1200Count

Maintenance

Statistics

CD Total user count

Sanding

Deep

Medium

Light

Abrasion

Coating

:

:

:

:

:

:

Maintenance

Statistics

Motor total work time

Sanding

Platen

Water

Compound

Coating

Vacuum

1500h30m53s

1400h45m42s

2000h32m38s

350h40m15s

250h40m15s

10h20m25s

:

:

:

:

:

:

Return

Maintenance

Statistics

Error Count

Turret Position

Grabs Position

Disc Out Cartridge

Disc Loading

Disc Release

Splash Cover

********

Plates Lift Position

Cartridge Position

Cartridge Full

Disc Unstoring

6Count

0Count

2Count

4Count

8Count

2Count

4Count

5Count

13Count

0Count

7Count

Return

Maintenance

Statistics

Error Count

Any Disc Release

No Sanding Pad

Disc Unloading

********

Water Recycle Low Volt

Turret Sensor

Sanding Pressure Lack

Water Leaking

SYSTEM ERROR

Sanding Motor Over Load

Sanding Motor Wire Down

0Count

2Count

21Count

0Count

0Count

1Count

0Count

3Count

3Count

3Count

3Count

Maintenance

Statistics

Error Count

Sanding Motor Non Stop

********

Sanding Motor Not Ready

Sanding Motor Ready

Platen Motor Over Load

Platen Motor Wire Down

Platen Motor Non Stop

********

Platen Motor Not Ready

Platen Motor Ready

Platen Motor Turn Lock

0Count

0Count

0Count

0Count

0Count

0Count

0Count

0Count

0Count

0Count

0Count

Maintenance

Touch Panel

Point of Intersection

X = 160, Y = 120

You Push Point  X = 160, Y = 120

Calibration

Return

Push the tip of the arrow

in the numerical order.

1

2

3

4

DIP SW1

DIP SW2

Maintenance

Calibration

Date and Time

Year (0-99)

Month (1-12)

Day (1-31)

Week (0:SUN-6:SAT)

Hour (0-23)

Minute (0-59)

Second (0-59)

Return

SET

3

24

15

8

4

4

7

Maintenance

Date and Time

24/04/03(THU) 15:07:22

Calibration

Return

Maintenance

Calibration

Date and Time

Year (0-99)

3

Cancel

0

7

8

9

4

5

6

1

2

3

0

C

E

2

1

10

11

9

7

8

12

3

6

5

4

1: CPU

RISC 32bit Micro controller

HD6417615ARF / HD6417616RF

(HITACHI)

Device controls all mechanical part and LCD.

2: EEPROM

Serial EEPROM  24LC128  (32kbyte)

Parameters are saved in this device.

If changing Main Board, remove and keep this device and set to new Main Board again.

3: SRAM

4Mbit High speed Static RAM

4: PIC

RISC 8bit Micro controller

PIC16F877 (Microchip)

Device controls Sanding Motor and Platen Motor.

5: Sensor Interface

Interface part of Sensors in machine.

All sensors are provided with 26VDC.

6: LCD Interface

Interface part of control LCD and Touch Panel.

Water pump (M7) Driver

7: DC Motor Drivers

TA8428K(S)  (TOSHIBA)

Device controls Pumps and Turret Motor.

Turret Motor (M5) Driver

Coating pump (M9) Driver

Compound pump (M8) Driver

8: Stepping Motor Drivers

Devices are inside of Heat sink.

TA8435H (TOSHIBA): Loading Motor, Lift Motor, and Changer Motor

SLK7033M (SANKEN): Platen Motor

Platen Motor (M2) Driver

Changer Motor (M6) Driver

Loading Motor (M3) Driver

Lift Motor (M1) Driver

9: 7Seg LED

Indicated software progress and messages.

10: DIP Switch

Setting special mode for the software.

Each bit has meaning.

DIP SW1

DIP SW2

ON

1  2  3  4  5  6  7  8

ON

1  2  3  4  5  6  7  8

DIP SW1

DIP SW2

11: Reset Switch

By pushing this button, CPU and all devices are reset.

12: FROM

Main program is stored in this device.

6

4

5

10

11

12

13

7

8

9

3

1

2

5

4

9

8

7

6

1

2

3

5103TL

5241TL

5558TL

5556TL

5558T2L

5556T2L

BXH-0001T-P0.6

Pin No.5

Pin No.1

- Open the hatch and loosen and remove two screws that are both side of hatch module.

- Remove 4 screws that are fixed between unit to Main body and 2 connectors.

- Open the hatch slowly.

- Take out the unit carefully.

- Remove the Front Cover. Two screws are bottom and more two screws are both side of this cover.

- Remove the screw for fixing the Lock and Thumb knobs.

- Remove the connector and take out the unit carefully.

Thumb Knob

Lock

Wire Bracket

- Remove Wire Pusher and Wire Bracket by loosen each one screw.

- Remove the connector.

- Remove two Thumb knobs that are fixed this unit.

- Take out the unit carefully.

Wire Pusher

- Remove two Thumb knobs that are fixed this unit.

- Remove the connectors and ground cable between this unit to Main body.

- Remove the unit carefully.

Ground Wire

- Remove two Thumb knobs that are fixed this unit.

- Remove the unit carefully.

- Remove the connector.

deflection

spring